December 3, 2013

Dennis B. Martin

Facilities Manager

United States Marine Corps

Marine Barracks

8th & I Streets SE

Washington, DC 20390

RE:	Permit Nos. 6321-R1, 6322-R1, and 6323-R1  to Operate Three (3) 8.37 MMBtu per Hour Natural Gas Fired Water Tube Boilers at the United States Marine Corps Barracks

Dear Mr. Martin:

Pursuant to section 200.2 of Title 20 of the District of Columbia Municipal Regulations (20 DCMR), a permit from the District Department of the Environment (the Department) shall be obtained before any person can operate a stationary source in the District of Columbia. The application of the United States Marine Corps (the permittee) to operate  three (3)  natural gas fired boilers 1, 2, and 3 (serial numbers 15578-1, 15578-2 and 15578-3, respectively), located at the Marine Barracks, BEQ, Building #20, 8th and I Streets SE, in Washington, DC, have been reviewed.

Based on the plans and specifications as detailed in the air permit renewal application submittal and its update received on June 28, 2013, and August 23, 2013, respectively, the applications are hereby approved, and the operation of the boilers is permitted, subject to the following conditions:

I.	General Requirements:

  - The approval is issued pursuant to the applicable air pollution control requirements of 20 DCMR for the operation of the steam boilers.

b.	This set of permits will expire on December 2, 2018.  If continued operation after this date is desired, the owner or operator shall submit application for renewal by September 2, 2018. [20 DCMR 200.4]

c.	Operation of equipment under the authority of this set of permits shall be considered acceptance of its terms and conditions.

- The permittee shall allow authorized officials of the District, upon presentation of identification, to:

1.	Enter upon the permittee’s premises where a source or emission unit is located, an emissions related activity is conducted, or where records required by this permit are kept;

2.	Have access to and copy, at reasonable times, any records that must be kept under the terms and conditions of this permit;

3.	Inspect, at reasonable times, any facilities, equipment (including monitoring and air pollution control equipment), practices, or operations regulated or required under this permit; and

4.	Sample or monitor, at reasonable times, any substance or parameter for the purpose of assuring compliance with this permit or any applicable requirement.

- This permit shall be kept on the premises and produced upon request.

- Failure to comply with the provisions of this permit document may be grounds for suspension or revocation. [20 DCMR 202.2]

II.	Emission Limitations:

  - The total annual emissions of criteria pollutants from the three boilers in aggregate shall not be greater than those specified in the following table [20 DCMR 201]:

| Pollutant | Annual Emissions Limit (ton/yr) |
| --- | --- |
| Carbon Monoxide (CO) | 8.790 |
| Oxides of Nitrogen (NOx) | 10.470 |
| Particulate Matter | 0.795 |
| Volatile Organic Compounds (VOC) | 0.567 |
| Sulfur Dioxide (SO2) | 0.063 |

  - b.	Visible emissions shall not be emitted into the outdoor atmosphere from the boilers, except that discharges not exceeding forty percent (40%) opacity (unaveraged) shall be permitted for two (2) minutes in any sixty (60) minute period and for an aggregate of twelve (12) minutes in any twenty-four hour (24 hr.) period during start-up, cleaning, adjustment of combustion controls, or malfunction of the equipment [20 DCMR 606.1]

c.	An emission into the atmosphere of odorous or other air pollutants from any source in any quantity and of any characteristic, and duration which is, or is likely to be injurious to the public health or welfare, or which interferes with the reasonable enjoyment of life or property is prohibited. [20 DCMR 903.1]

d.	Particulate matter emissions from the boilers shall not exceed 0.060 pound per million BTU.  (The Permittee is deemed to have complied with this requirement by complying with Condition III(a) of this permit) [20 DCMR 600.1]

III.	Operational Limitations:

  - a.	Only natural gas shall be used as fuel in the boilers covered by this permit.  No other fuels are approved for use. [20 DCMR 201].

  - b. 	This approval is valid for the specific activity cited in the application submitted to this office.  Any deviation from the specific activity is a violation of the permit.

c.	The boiler shall be operated at all times in a manner consistent with the manufacturer’s specifications for the equipment. [20 DCMR 201]

d.	At all times, including periods of startup, shutdown, and malfunction, the owner or operator shall, to the extent practicable, maintain and operate each boiler in a manner consistent with good air pollution control practice for minimizing emissions.  Determination of whether acceptable operating procedures are being used will be based on information available to the Department which may include, but is not limited to, monitoring results, opacity observations, review of operating and maintenance procedures, and inspection of the source. [20 DCMR 201]

IV.	Monitoring and Testing Requirements:

a.	The permittee, shall monitor the operation of the boilers in a manner consistant with a good preventive maintenance program.

b.	The permittee shall monitor the type and amount of fuel burned in the boilers.

c.	The permittee shall monitor the stack outlets and identify any visible emissions to ensure that if they occur, the problem is promptly identified and repaired.

d.	The permittee shall conduct and allow the Department access to conduct tests of air pollution emissions from any source, as requested. [20 DCMR 502.1]

V.	Record Keeping:

The following information shall be recorded and maintained in a log at the facility for a period not less than three years. [20 DCMR 500.8]

a.   The Permittee shall keep records of fuel use for the boilers, showing therms or standard cubic feet of natural gas combusted in each boiler, each month.  These records shall be kept as a 12-month rolling sum.

b.	The permittee shall keep records of all maintenance performed on the emission units so as to document compliance with Conditions III(c) and (d).  These records shall be initialed to attest to their accuracy.

c.	The permittee shall keep records of the results of any visible emissions monitoring performed.

d.	The permittee shall keep records of the results of any testing the permittee performed pursuant to Condition IV(d).

VI. Record Keeping:

  - The permittee shall immediately contact the Air Quality Division’s Permitting Branch upon becoming aware of a sudden equipment failure or emergency or emissions in excess of any emission limit.

b.	The permittee shall report the fuel usage and the criteria pollutants emissions from the boilers to the Air Quality Division’s Permitting Branch upon request.

c.	In addition to complying with Condition VI(a) and any other reporting requirements mandated by the District of Columbia, the owner or operator shall, within thirty (30) calendar days of becoming aware of any occurrence of excess emissions, supply the Department in writing with the following information:

    - The name and location of the facility;

    - The subject source(s) that failed, experienced the emergency, or caused the excess emissions;

    - The time and date of the first observation of the equipment failure, emergency, or excess emissions;

    - The cause and estimate/expected duration of the excess emissions (if applicable); and

    - The proposed corrective actions and schedule to correct the conditions causing the emergency or excess emissions.

If you have any questions, please call me at (202) 535-1747 or Abraham T. Hagos at (202) 535-1354.

Sincerely,

Stephen S. Ours, P.E.

Chief, Permitting Branch

SSO:ATH