April 30, 2013

Mr. James Schrote, 				Permittee: The George Washington University

Executive Director, Facilities

The George Washington University

Operations Division

2025 F Street, NW, Suite 215

Washington, DC 20052

RE:	Permits to Operate South Hall Natural Gas Fired Hot Water Boilers

Dear Mr. Schrote:

Pursuant to sections 200.1 and 200.2 of Title 20 of the District of Columbia Municipal Regulations (20 DCMR), a permit from the District Department of the Environment (the Department) shall be obtained before any person can construct and operate a stationary source in the District of Columbia. The Permittee’s applications to operate the listed three Bryan natural gas hot water boilers, located in Washington, DC, have been reviewed:

| Equipment Location | Address | Equipment Size (MMBtu/hr Heat Input) | Serial Number | Permit No. |
| --- | --- | --- | --- | --- |
| South Hall | 2135 Street NW Washington, DC | 6.0 | 96525 | 6696 |
| South Hall | 2135 Street NW Washington, DC | 6.0 | 96561 | 6697 |
| South Hall | 2135 Street NW Washington, DC | 6.0 | 96559 | 6698 |

Based on the submitted plans and specifications as detailed in the applications received on November 1, 2012, the applications are hereby approved, and the operation of the hot water boilers is permitted, subject to the following conditions:

I.	General Requirements:

  - The approval is issued pursuant to the applicable air pollution control requirements of 20 DCMR for the operation of the heating boilers.

b.	This set of permits will expire on April 29, 2018.  If continued operation after this date is desired, the owner or operator shall submit applications for renewal by January 29, 2018. [20 DCMR 200.4]

c.	Operation of equipment under the authority of this set of permits shall be considered acceptance of its terms and conditions.

- The Permittee shall allow authorized officials of the District, upon presentation of identification, to:

1.	Enter upon the Permittee’s premises where a source or emission unit is located, an emissions related activity is conducted, or where records required by this permit are kept;

2.	Have access to and copy, at reasonable times, any records that must be kept under the terms and conditions of this permit;

3.	Inspect, at reasonable times, any facilities, equipment (including monitoring and air pollution control equipment), practices, or operations regulated or required under this permit; and

4.	Sample or monitor, at reasonable times, any substance or parameter for the purpose of assuring compliance with this permit or any applicable requirement.

- This set of permits shall be kept on the premises and produced upon request.

- Failure to comply with the provisions of this permit document may be grounds for suspension or revocation. [20 DCMR 202.2]

g.	Emergency situations shall be handled in accordance with the provisions of 20 DCMR 302.7 (a) through (c).

h.	If not already completed by the date of this permit, within twelve (12) months of issuance of this permit to operate, the Permittee shall submit a complete application to modify the facility’s Title V operating permit to include the requirements of this set of permits [20 DCMR 301.1(a)(3)].  This application is due by March 5, 2014.

II.	Emission Limitations:

  - Each of the three (3) identical 6.0 million BTU per hour natural gas boilers identified as SH-B1, SH-B2 and SH-B3, shall not emit pollutants in excess of those specified in the following table [20 DCMR 201]:

| Pollutant | Short-Term Limit (Natural Gas) (lb/hr) | Annual Emissions Limit (ton/yr) |
| --- | --- | --- |
| Carbon Monoxide (CO) | 0.49 | 2.16 |
| Oxides of Nitrogen (NOx) | 0.59 | 2.58 |
| Particulate Matter < 10 microns (PM10) | 0.04 | 0.19 |
| Volatile Organic Compounds (VOC) | 0.0323 | 0.14 |
| Sulfur Dioxide (SO2) | 0.0035 | 0.015 |

  - b.	Particulate matter emissions from boilers SH-B1, SH-B2, and SH-B3 shall not exceed 0.11 pounds per million BTU on a per boiler basis. [20 DCMR 600.1]

c.	Visible emissions shall not be emitted into the outdoor atmosphere from each boiler; except that no greater than 40% opacity (unaveraged) shall be permitted for two minutes per hour and for an aggregate of twelve minutes per 24-hour period during start-up, cleaning, soot blowing, adjustment of combustion controls, or malfunction.[20 DCMR 606.1]

d.	An emission into the atmosphere of odorous or other air pollutants from any source in any quantity and of any characteristic, and duration which is, or is likely to be injurious to the public health or welfare, or which interferes with the reasonable enjoyment of life or property is prohibited. [20 DCMR 903.1]]

III.	Operational Limitations:

  - a.	The sole fuel for the boilers shall be natural gas with a maximum sulfur content of 2.5 grains per 100 standard cubic feet.   [20 DCMR 201]

- The boilers shall be operated at all times in a manner consistent with the manufacturer’s specifications for the equipment. [20 DCMR 201]

IV.	Monitoring and Testing Requirements:

a.	If a stack test to determine compliance with Condition II (a), (b), and/or (d) is requested by the Department in accordance with 20 DCMR 502.1, the written report of the results of such a stack test shall be furnished to the District in accordance with the following requirements [20 DCMR 502]

1.	One (1) original and one (1) copy of the test protocol shall be submitted to the following address a minimum of thirty (30) days in advance of the proposed test date.  The test shall be conducted in accordance with Federal and District requirements.

Chief, Compliance and Enforcement Branch

Air Quality Division

1200 First Street NE

5th Floor

Washington, DC 20002

2.	The test protocol shall be approved by the Department prior to initiating any testing.  Upon approval of the test protocol, the Company shall finalize the test date with the assigned inspector in the Permitting and Enforcement Branch.  The District must have the opportunity to observe the test for the results to be considered for acceptance.

3.	The final results of the testing shall be submitted to the Department within sixty (60) days of the test completion.  One (1) original and one (1) copy of the test report shall be submitted to the address in Condition IV (a)(1) above.

4.	The final report of the results shall include the emissions test report (including raw data from the test) as well as a summary of the test results and a statement of compliance or non-compliance with permit conditions to be considered valid.  The summary of results and statement of compliance or non-compliance shall contain the following information:

A.	A statement that the owner or operator has reviewed the report from the emissions testing firm and agrees with the findings.

B.	Permit number(s) and condition(s) which are the basis for the compliance evaluation.

C.	Summary of results with respect to each permit condition.

D.	Statement of compliance or non-compliance with each permit condition.

5.	The results must demonstrate to the Department’s satisfaction that the emission unit is operating in compliance with the applicable regulations and conditions of this permit; if the final report of the test results shows non-compliance the owner or operator shall propose corrective action(s).  Failure to demonstrate compliance through the test may result in enforcement action.

b.	The owner or operator shall conduct and allow the Department access to conduct tests of air pollution emissions from any source as requested.  [20 DCMR 502.1]

c.	At least once per month, during operation of each boiler, the Permittee shall conduct visual observations of the emissions from each boiler.  If no operations are occurring for a given boiler during a given month, this shall be so noted.  If emissions are visible, the Permittee shall make arrangements for prompt visible emissions testing by a person certified in accordance with EPA Reference Method 9 (40 CFR 60, Appendix A).  Such a test shall consist of a minimum of 30 minutes of opacity observations for the boiler in question.

d.	Regardless of whether or not emissions are observed pursuant to Condition IV (c) of this permit, the Permittee shall conduct a minimum of one visible emissions test of each boiler each year for the fuel burned that year.  Such a test program shall consist of a minimum of 30 minutes of opacity observations of each boiler and shall be performed by a person certified in accordance with EPA Reference Method 9 (40 CFR 60, Appendix A).

V.	Record Keeping and Reporting Requirements:

The following information shall be maintained at the facility for a period not less than five (5) years [20 DCMR 500.8 and 20 DCMR 302.1(c)(2)(B)]:

a.	The Permittee shall keep records of the results of all emissions testing and sampling required for the boilers pursuant to Conditions IV (a), (b), (c), and (d) of this permit document.

b. 	The Permittee shall maintain records of the amount of fuel used each month in each boiler.  These data shall be maintained in a rolling twelve month sum format [20 DCMR 500.2]

If you have any questions, please call me at (202) 535-1747 or John Nwoke at (202) 724-7778.

Sincerely,

Stephen S. Ours, P.E.

Chief, Permitting Branch

SSO:JCN