##### January 5, 2016

Neal Mohlmann, Chief

Office of Environment and Safety

U.S. Department of the Treasury

Bureau of Engraving and Printing

14th and C Streets, SW

Washington, D.C. 20228

Dear Mr. Mohlmann:

Re:	Permit (#6589-R1) to Operate One (1) Sheet Fed, Non-Heatset, Offset, Lithographic, Komori 5 Color Printing Press at the Bureau of Engraving and Printing

Pursuant to §200.1 and §200.2 of Title 20 of the District of Columbia Municipal Regulations (20 DCMR), a permit shall be obtained from the Department of Energy and Environment (the Department) before any person may cause or allow the construction or operation of a stationary source in the District of Columbia.  The request of the U.S. Department of the Treasury, Bureau of Engraving and Printing (the Permittee) to operate one (1) Komori 5 Color, sheet fed, non-heatset, offset, lithographic printing press on the 3rd floor, B-wing, of the Main Building at 14th and C Streets SW, per the application, dated August 24, 2015, is hereby granted subject to the following conditions:

I.    General Requirements:

a.	The sheet fed, non-heatset, offset, lithographic, Koromi 5 Color, printing press shall be operated in compliance with applicable air pollution control requirements of 20 DCMR.

b.	This permit expires on January 4, 2021 (20 DCMR 200.4).  If continued operation after this date is desired, the owner or operator shall submit an application for renewal by October 4, 2020.

c.	Operation of equipment under the authority of this permit shall be considered acceptance of its terms and conditions.

d.	The Permittee shall allow authorized officials of the Department, upon presentation of identification, to:

1.	Enter upon the Permittee’s premises where a source or emission unit is located, an emissions related activity is conducted, or where records required by this permit are kept;

2.	Have access to and copy, at reasonable times, any records that must be kept under the terms and conditions of this permit;

3.	Inspect, at reasonable times, any facilities, equipment (including monitoring and air pollution control equipment), practices, or operations regulated or required under these permits; and

4.	Sample or monitor, at reasonable times, any substance or parameter for the purpose of assuring compliance with this permit or any applicable requirement.

e.	This permit shall be kept on the premises and produced upon request.

f. 	Failure to comply with the provisions of these permits may be grounds for suspension or revocation. [20 DCMR 202.2]

g.	If not already completed, within three (3) months of issuance of this permit to operate, the Permittee shall submit a complete application to modify the facility’s Title V operating permit to include the requirements of this permit. [20 DCMR 301.1(a)(3)].

II.   Emission Limitations:

a.	The maximum annual emissions of volatile organic compounds (VOC) resulting from the operation of the press shall not exceed 0.97 tons per year.

b.	Visible emissions shall not be emitted into the outdoor atmosphere from the press. [20 DCMR 606.1]

c.	An emission into the atmosphere of odorous or other air pollutants from any source in any quantity and of any characteristic, and duration which is, or is likely to be injurious to the public health or welfare, or which interferes with the reasonable enjoyment of life or property is prohibited . [20 DCMR 903]

III.	Operational Limitations:

- The Permittee shall not use, in conjunction with this printing press, cleaning solutions containing VOCs in excess of  ten millimeters of mercury (10 mm Hg) at twenty degree Celsius (20o C or 68o F) of VOC composite partial pressure calculated as follows [20 DCMR 716.8]:

where:

Ppc 	= 	VOC composite partial pressure at twenty degrees Celsius (20°C) or sixty-eight degrees Fahrenheit (68º F), in mm Hg;

Wi 	= 	Weight of the "i"th VOC compound, in grams, as determined by ASTM E 260-91;

Ww 	= 	Weight of water, in grams as determined by ASTM D 3792-86;

We 	= 	Weight of the "i"th exempt compound, in grams, as determined by ASTM E 260-91;

Mwi 	= 	Molecular weight of the "i"th VOC compound, in grams per g-mole, as given in chemical reference literature;

Mww	= 	Molecular weight of water, eighteen grams (18 g) per g-mole;

Mwe 	= 	Molecular weight of the "i"th exempt compound, in grams per g-mole, as given in chemical reference literature; and

Vpi 	= 	Vapor pressure of the "i"th VOC compound at twenty degrees Celsius (20º C) or sixty-eight degrees Fahrenheit (68º F), in mm. Hg, as determined in accordance with ASTM test method ASTM D2879-86 or other method identified as acceptable pursuant to 20 DCMR 747.6.

b.   The Permittee shall not utilize fountain solution in conjunction with the press in excess of five percent (5%) alcohol (by weight) in the fountain, or to achieve an equivalent level of control, any one of the following shall occur [20 DCMR 716.6(c)]:

1.   Reduce the on-press (as-applied) alcohol content to five percent (5%) alcohol or less (by weight);

2.	Use eight and half percent (8.5%) alcohol or less (by weight) on-press (as-applied) in the fountain solution, provided the solution is refrigerated to less than sixty degree Fahrenheit (60º F) or sixteen degree Celsius (16º C); or

3.	Use an alcohol substitute so that the on-press (as applied) VOC content is five percent (5%) or less (by weight) as determined by EPA Method 24 and no alcohol is in the fountain solution.]

c.   All containers holding VOC containing materials shall be open only when necessary and openings shall be restricted to the extent feasible. [20 DCMR 716.21]

d.	Cleaning solutions and shop towels used for cleaning shall be kept in closed containers. [20 DCMR 716.9]

e.   The leaking of any solvent or solvent-containing material from any printing unit or associated equipment is prohibited. [20 DCMR 716.22]

f.   The storage or disposal of any solvent-containing material, including waste material, in a  manner that will cause or allow its evaporation into the atmosphere is prohibited. [20 DCMR 716.23]

g.   To the greatest extent feasible, persons operating printing unit and associated equipment shall minimize their use of VOC containing materials by restricting wasteful usage and by replacing the material with emulsions or other materials. [20 DCMR 716.24]

h.	At all times, including periods of startup, shutdown, and malfunction, the owner shall, to the extent practicable, maintain and operate the unit in a manner consistent with good air pollution control practice for minimizing emissions.  Determination of whether acceptable operating procedures are being used will be based on information available to the Department which may include, but is not limited to, monitoring results, opacity observations, review of operating and maintenance procedures, and inspection of the source.

IV.	Monitoring and Testing Requirements:

a.	The Permittee shall monitor the types, constituents, characteristics, and quantities of inks, cleaning solvents, and fountain solutions used on the press to ensure compliance with Conditions III(a) and (b).  Testing for the VOC content of inks shall be performed in accordance with EPA Reference Method 24 (40 CFR 60, Appendix A).

b.	To show compliance with Condition III(a), the Permittee shall perform one of the following:

1.	 Perform testing of each cleaning solution used in accordance with EPA Reference Method 24 (40 CFR 60, Appendix A) that is to be used in the unit prior to initial use and semi-annually thereafter; or

2.	Perform testing or obtain and review accurate documentation for each cleaning

Solution showing that the composite partial pressure of all VOC’s contained in each solution is not greater than 10 mm Hg at 20º C. The composite partial pressure is to be calculated pursuant to the equation in Condition III(a).

c.	The Permittee shall monitor the use of storage containers for VOC and solvents-containing materials to ensure compliance with Condition III(c).

d.	The Permittee shall monitor the use of cleaning solutions and shop towels to esure compliance with Condition III(d).

e.	The Permittee shall monitor the status of the press and associated equipment to ensure that    no leaking is occurring and that they are being properly operated to ensure compliance with Condition III(e).  Any leaks identified shall be repaired promptly.

f.	In addition to general monitoring, at least once per quarter, the Permittee shall perform a thorough inspection of the press, associated equipment, and all solvent storage containers to ensure compliance with Conditions III(e) and (h).  Any leaks identified shall be repaired promptly.

g.	The Permittee shall monitor the emission points for visible emissions as needed to ensure compliance with Condition II(b).

h.	The Permittee shall monitor the facility for compliance with the nuisance and odor requirements of Condition II(c).

i.	The Permittee shall conduct and allow the Department access to conduct tests of air pollution emissions from any source as requested. [20 DCMR 502.1]

V.	Record Keeping Requirements:

The following information shall be maintained at the facility for a period not less than three (3) years [20 DCMR 500.8] and shall be made available to the Department upon written or verbal request:

a.	The Permittee shall maintained records of the types, constituents, characteristics, and quantities of inks, cleaning solutions, and dampening solutions used on the press to show compliance with Conditions III(a) and (b).

b.	The Permittee shall maintain records of the results of testing or the records of the manufacturers’ documentation obtained pursuant to Conditions III(a) and IV(b).  Chains of custody for all samples shall be required as part of the testing records required.

c.	The Permittee shall maintain records of any leaks identified pursuant to Conditions IV(c) as well as the actions taken to halt any leaking identified.

d.	The Permittee shall maintain records of the results of the quarterly (or more frequent) inspections of the press, associated equipment, and solvent storage containers performed pursuant to Condition IV(d).  These records shall identify the inspector(s) who performed the inspections and these inspectors shall sign or initial the records to certify that they performed the complete inspection and that the records represent the results of the inspection.

e.	The Permittee shall keep records of any occurrences of visible emissions from the emission points of these units as well as any actions taken to correct the problem.

f.	The Permittee shall keep records of any occurrences of exceedances of the requirements of Condition II(c) and any odor complaints received.  The Permittee shall also keep records of the actions taken to correct any identified odor or nuisance pollutant exceedances.

g.    The Permittee shall keep records, updated monthly, of the average VOC emissions per hour of press operation that month from each of the following sources:

1.	inks; and

2.	solvents.

(Note: these records shall be used to determine compliance with Conditions II(a) and (b) of this permit.  They shall be updated within seven (7) days of the end of each calendar month.)

h.	The Permittee shall keep records of the maintenance performed on the press and associated equipment.

i.	The Permittee shall keep records of the results of any testing required pursuant to Condition IV(i).

VI.	Reporting Requirements:

a.	A copy of the most recent analytical results of the ink samples or other documentation kept pursuant to Condition IV(a) shall be submitted to the Department with the Permittee’s Title V semi-annual and annual reports for the ink used during the reporting period.

b.	Emissions in excess of any emission limits shall be reported by telephone, immediately upon discovery, to the Air Quality Division’s Compliance and Enforcement Branch.

c.	In addition to complying with Condition VI(b) and any other reporting requirements mandated by the 20 DCMR, the owner or operator shall, within thirty (30) calendar days of becoming aware of any occurrence of excess emissions, supply the Department in writing with the following information:

1.	The name and location of the facility;

2.	The subject source(s) that caused the excess emissions;

3.	The time and date of the first observation of the excess emissions;

4.	The cause and estimated/expected duration of excess emissions;

5.	For sources subject to numerical emission limitations, the estimated rate of      emissions (expressed in the units of the applicable emission limitation) and the operating data and calculations used in determining the magnitude of the excess emissions; and

6.	The proposed corrective actions and schedule to correct the conditions causing the excess emission.

If you have any questions, please me at (202) 535-1747 or Abraham T. Hagos at (202) 535-1354.

Sincerely,

Stephen S. Ours, P.E.

Chief, Permitting Branch

SSO:ATH